## Slide 1: ELECTRICITY
A CLIL MODULE
Level A2

## Slide 2: TOPIC
Electricity
Electric circuits and circuit symbols
Ohm’s Law
Series and Parallel Circuits

## Slide 3: AIM
The students will able:
to explain how electric current flows in a circuit
to wire a basic circuit
to take measurements of voltage and current intensity in a circuit
to explain the difference between series and parallel connections

## Slide 4: What is electricity?
The Electricity is the physical phenomena associated with the flow or movement of electric charge.
electric charge
conductor
atom
-
+

## Slide 5: ELECTRIC CHARGE
Electric charge as a fundamental property of some subatomic particles.
Inside an atom there are:
- Protons have a positive charge
- Electrons have a negative charge
- Neutrons have no charge (neutral)

## Slide 6: COULOMB
Particles of opposite charges are attracted to each other
Particles of equal charges are repelled
The SI (Systeme International) unit for charge is the coulomb (C)
It takes 6.25 x 1018 protons to equal one coulomb!

## Slide 7: CONDUCTOR AND INSULATOR
A conductor is something which freely allows the motion of electric charge.
An insulator is the opposite; it greatly resists the flow of charge.
Conductors
eg. Copper cable
Water – Gold Silver – Platinum Metals
Insulators
eg. Plastic sheet
Rubber – Ceramic Wood

## Slide 8: ELECTRIC CURRENT
Electric current is the ordered flow of negative electric charge.
Typically the negative electric charge is electrons.
In fact “conventional current” , which is what is used by all electrical engineers, is the flow of positive charge.
conventional current
flow of electrons

## Slide 9: How electricity works?
https://www.youtube.com/watch?v=mc979OhitAg

## Slide 10: ELECTRIC CURRENT
In a conductor the electric charges are free to move, then there is passage of electric current
In an insulator the electric charges they are not free to move, then there is no passage of electric current

## Slide 11: AMPERE
The SI unit of Intensity of electric current ( I ) is the Ampere (A).
Ampère is equal to a flow of one coulomb per second.
Intensity current is measured with an ammeter
Digital ammeter
(digital multimeter)
has a digital display
Analogic ammeter
has a graduated scale

## Slide 12: ELECTRIC VOLTAGE
Current can only flow in the presence of an electric field, often provided by a voltage source (eg. Battery or Cell).
Voltage is the electric potential between two points (∆V) .
It is the electric potential to cause an electric current to flow.

## Slide 13: VOLT
Voltage is measured with a voltmeter.
The SI unit for voltage is the volt (V).
Volt measures how strongly an electrical current is sent around an electrical circuit.
Digital voltmeter
(digital multimeter)
has a digital display
Analogic voltmeter
has a graduated scale

## Slide 14: VOLT
How many volts are in a AA battery?
1.5 V
the wall outlet?
230 V
the power lines in the street?
about 13,000 V
the large power lines?
up to 765,000 V
lightning?
about 100,000,000 V

## Slide 15: ELECTRIC CIRCUIT
Define the electric circuit as a connection of two or more components to form a closed loop.
The closed loop is necessary to allow the electric current to flow from one point of the voltage source to the other.

## Slide 16: ELECTRIC RESISTANCE
Electric resistance is a physical property which describes how well electric current flows in a material.

## Slide 17: OHM
The SI unit for resistance is the ohm (Ω)
The resistor has resistance equal to 1Ω when, subjected to a potential difference of 1V. It’s transmitted a current of 1A.
Electric resistance is measured with an instrument called ohmmeter
Digital ohmmeter
(digital multimeter)
Analogic ohmmeter

## Slide 18: First Ohm’s Law
Voltage = Resistance ∙ Current
“The voltage DV between the ends of a metallic conductor is directly proportional to the intensity of the current that runs through it”.
One therefore has:
where the coefficient of resistance of the conductor R is constant with changing DV.
Ohm’s Law is a formula used to calculate the relationship between voltage, current and resistance in an electrical circuit.

## Slide 19: Ohm’s Pyramid
If two of these values are known, technicians can reconfigure Ohm’s Law to calculate the third. Just modify the pyramid as follows:
If you know current (I) and resistance (R) and want to know voltage (E), multiply the bottom halves of the pyramid

## Slide 20: Ohm’s Pyramid
If you know voltage (E) and current (I) and want to know resistance (R), X-out the R in the pyramid and calculate the remaining equation
If you know voltage (E) and resistance (R) and want to know current (I), X-out the I and calculate the remaining equation

## Slide 21: Ohm’s Pyramid
What is the current in the circuit?
I =
What is the resistance created by the lamp?
R =
What is the voltage in the circuit?
E = I ∙ R = (5A) ∙ (8Ω) = 40 V
EXAMPLES OF APPLICATION OF THE OHM’S LAW

## Slide 22: Ohm’s law
https://www.youtube.com/watch?v=HsLLq6Rm5tU

## Slide 23: ELECTRIC POWER
Define electric power as the rate at which electrical energy is transferred.
The SI unit for power is the watt (W).
Power = Voltage ∙ Current
Voltage = Power / Current
Current = Power / Voltage
The pyramid

## Slide 24: Refresh the main topic
https://www.youtube.com/watch?v=HsLLq6Rm5tU&t=355s

## Slide 25: Excercise
Do the excercise in couple.

## Slide 26: SERIES CIRCUIT
In a series circuit, electric current has only one path to follow.
All parts are connected one after another. Electrons flow from the negative side of the battery around in a loop to the positive side.

## Slide 27: SERIES CIRCUIT
Series components are connect in line with each other.
  they share the same current
  Components in series have the same current
  They divide the voltage among themselves
  Components in series have different voltages
  The different voltages add up to the original total voltage of the voltage source

## Slide 28: PARALLEL CIRCUIT
In a parallel circuit, electric current has more than one path to follow.
Electrons can follow different paths as they flow from the negative side of the battery to the positive side.

## Slide 29: PARALLEL CIRCUIT
Parallel components are connected side by side.
Each component provides a different path for the current to flow
Components in parallel have different currents
The different currents add up to the current in the voltage source
Components in parallel have the same voltage

## Slide 30: Watch the video
Series circuit:
https://www.youtube.com/watch?v=VV6tZ3Aqfuc
Parallel circuit:
https://www.youtube.com/watch?v=5uyJezQNSHw&t=547s

## Slide 31: Thanks for the attention
All the Materials, Videos and Images are for Didactic Purposes Only”.